Freedom of Information Act 2000 (FOIA) /Environmental Information Regulations 2004 (EIR) - Cofresh

Your request for information has now been considered and the Council’s response to your questions is shown below.

You asked:

1. Records of complaints from local residents concerning odour nuisance from the site from 29 August 2019 to date. We are aware that you will need to redact the personal information of complainants but please leave visible the street names from which the complaints originate;

Answer:

Please see attached file listing all complaints within this time period.

2. Correspondence passing between the council and the site regarding odour complaints; the investigations of source of odour and measures taken to abate the odour;

Information relating to this question are found in the answer to question 4 below. As question 4 details the 3 site meetings held at the site on the 27th September 2019, 12th February 2020 and 16th March 2020.

3. Any notices served on the operator in relation to odour nuisance from the site between 29 August 2019 to date;

None

4. Any records, attendance notes, memos, reports (or similar) relating to the monitoring/site inspections/site visit carried out in relation to odour nuisance from the site from 29 August 2019 to date;

27/09/2019, Site meeting at Cofresh offices. Present at meeting TO, RM, PP (Managing Director) and RG (Consultant).

*Purpose of meeting was to confirm completion and commissioning of proposed odour abatement plant which was due on 19/09/19.

*Deadline not met for following reasons;

-Drainage access point on the premises not accessible so drainage had to be re-routed across courtyard towards public highway. This resulted in a redesign of the concrete platforms/base on which the plant would rest.

*Further delay was because the ductwork could not be assembled onsite because the components parts are just too big and cannot be accommodated on the factory site. The ducting is now being assembled offsite (Nuneaton) and will be transported to site.

*Even more delay has been due to poor weather conditions (high winds and heavy rains) rendering work at height too risky.

*RG forecasted works will be completed by end of October -mid November 2019. PP to provide N&P with weekly updates of progress of works.

*PP to convene meeting once the works have been completed. TO

12/02/2020. TO Site meeting with PP and GS (Project manager). Discussed new Venturi Scrubber system in details. Last Friday 31/01/2020 recirculating fan stopped working resulting is odour complaint. This happened because separation pads were clogged by grease probably insufficient caustic dosing. On 12/02/2020 Project Manager installed an automatic dosing pump/meter. GS advised that the installation phase and commissioning is now complete; Project Manager will now carry out a couple of training session of Cofresh staff on the performance monitoring before the system is handed over at the end of the month.

GS to email TO details of the manufacturer's maintenance and monitoring schedule.

16/03/2020, TO & RM held meeting with PP and H to discuss the performance of recently installed odour abatement system. TO pointed out that since the company confirmed that the system was up and running there has been instances of high odour levels e.g. on 07/02/2020 and 04/03/2020. PP replied that these events have been investigated and the company now understands why these happened. He added that the recirculating pump tripped on 07/02/2020, and on 05/03/2020 the PH level had drifted. The system has been fitted with an automatic dose meter which adds the caustic into the tank depending on the PH level. PP added the amount of caustic needed is determined manually. **There's still some confusion about what level of manual intervention is required in order for the dose meter to operate efficiently. PP stated that the company are cleaning the filters more regularly than recommended by the manufacturer. RM suggested that it would be reasonable to put in place a weekly cleaning program for the filters. PP added that he is considering a daily cleaning schedule whereby the filters are removed at the end of the day, soaked in caustic overnight and washed in the morning before being re-used.

RM asked what the company's contingency plan is in case this system does not achieve the desired outcome. PP responded that he has made financial provisions for a carbon filtration bed/chamber to be installed.

Old chutes at the rear of the factory are still being used for the crisp production.

TO asked the company had carried out in-house staff training on the maintenance and performance of the system. PP responded that two officers have been appointed with full responsibility for the system.

Full inspection of the site was not able to be undertaken due to the outbreak of Coronavirus, further date to be confirmed when safe to do so.

5. confirm the current position regarding the installation of the wet scrubber system which was anticipated to be completed November 2019;

The wet scrubber was installed and operational in February 2020.

6. details of the name and contact number of the local authority officer responsible for the site.

The site is not the responsibility of any single Local Authority Officer. The Noise and Pollution Control Team respond to complaints relating to odour.

This letter therefore acts as a refusal notice under Section 17(1) of the FOIA because, in accordance with Section 1(1) of the Act and Regulation 12(4)(a) of the EIR, this information is not held by the Council.

You may re-use the information under an Open Government Licence.

If you are dissatisfied with the handling of your request, please write to:

Internal Review

Information Governance & Risk

Leicester City Council

City Hall, 115 Charles Street

Leicester LE1 1FZ

info.requests@leicester.gov.uk